## Slide 1: Chapter 2
The image, its representations and properties
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 2: Image representations, a few concepts
Perspective projection geometry (透視投影幾何公式)
  f : focal length (焦距)
  x, y, z: the co-ordinates of the point X in a 3D scene
  u, v: the co-ordinates in the 2D image plane
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 3: Projection geometry (投影幾何)
http://cgunn3.blogspot.tw/2012/04/where-parallels-meet.html
http://page.math.tu-berlin.de/~gunn/pages/PGTalkImages/perspectiveDemo-04.png

## Slide 4: Image representations, a few concepts
The quality of a digital image can be measured by
  Spatial resolution (space)
    The proximity (接近) of image samples in the image plane
  Spectral resolution (color)
    The bandwidth (頻寬) of the light frequencies captured by the sensor
  Radiometric (輻射的) resolution (intensity)
    The number of distinguishable gray-levels
  Time resolution (temporal resolution)
    The interval between time samples at which images are captured

## Slide 5: Image digitization (影像數位化)
Sampling (取樣)
  A continuous image is digitized at sampling points.
    These sampling points are ordered in the plane, and their geometric relation is called the grid (網格).
    Grids used in practice are usually square or hexagonal (六邊形 ).
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 6: Grids
The Bayer color filter mosaic. (Very common RGB filter.) Each two-by-two submosaic contains 2 green, 1 blue and 1 red filter, each covering one pixel sensor.
https://en.wikipedia.org/wiki/Color_filter_array
A Bayer filter camera uses a color filter array attached to a monochomatic sensor. The bilinear demosaicing algorithm performs the color reconstruction according to the Figures shown above.
http://www.siliconsoftware.de/download/live_docu/RT5/en/feature_blocks/PSBayer12/PSBayer12_bilinear.html(??)

## Slide 7: Image digitization
Pixel
  One infinitely small sampling point in the grid corresponds to one picture element also called a pixel or image element in the digital image.
  Voxel (體素 )
    In a 3D image, an image element is called a voxel (volume element)
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 8: Quantization
The transition between continuous values of the image function (brightness) and its digital equivalent is called quantization (量化).
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 9: Digital image properties
Matric and topological properties of digital images
  Distance (Matric)
    Any function D holding the following three condition is a distance (or a metric)
      Identity (同一性)
      Symmetry (對稱性)
      Triangular inequatility (三角不等式)
    https://zh.wikipedia.org/wiki/%E5%BA%A6%E9%87%8F%E7%A9%BA%E9%97%B4
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
    D(p, q) = 0 iff p = q

## Slide 10: Matric and topological properties of digital images
Euclidean distance (歐氏距離)
City block distance (城市街區距離)
Chessboard distance (棋盤距離)
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 11: Matric and topological properties of digital images
Regions (區域)
  A region is a connected set.
  A region is a set of pixels in which there is a path between any pair of its pixels, all of those pixels also belong to the set.
  4-neighbors vs. 8-neighbors
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
http://ippr-practical.blogspot.com/2012/04/region-segmentation.html

## Slide 12: Matric and topological properties of digital images
Contiguous (接觸的;連續的)
  If there is a path between two pixels in the set of pixels in the image, these pixels are called contiguous.
  The relation ‘to be contiguous’ is reflexive (反身), symmetric (對稱), and transitive (遞移).
  ‘To be contiguous’ can be used to decompose an image into individual regions.
  For example, the character is decomposed into 3 regions.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 13: Matric and topological properties of digital images
Multiple Contiguous
  Let R be the union of all regions Ri (these regions do not touch the image bounds), and
  RC be the set complement of R with respect to the image.
  The subset of RC which is contiguous with the image bound is called the background, and the remainder of the complement RC is called holes.
  A region is called simple contiguous if it has no holes.
  The complement of a simply contiguous region is contiguous.
  A region with holes is called multiple contiguous.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 14: Matric and topological properties of digital images
The figure (a) shows two digital line segments with 45o slope.
  If 4-connectivity is used, the line are not contiguous at each of their points.
    Two perpendicular lines do intersect in one case (upper right intersection) and do not intersect in another case (lower left).
  One possible solution: to treat objects using 4-neighborhoods and background using 8-neighborhoods
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
4-neighbors
8-neighbors

## Slide 15: Matric and topological properties of digital images
Chamfer(導角;倒角) distance
  A simple application of the concept of distance
  For example, consider a binary image,
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 16: Algorithm 2.1: Distance transformation
Step 1: Choose a distance Nmax and initialize an image F.
  F: the pixels corresponding to the subset to be chamfered to 0, and all others to Nmax.
  Step 2: Pass through image pixels from top to bottom and left to right.
  For a given pixel, consider neighbors above and to the left and set
  Step 3: Pass through image pixels from bottom to top and right to left.
  For a given pixel, consider neighbors bottom and to the right and set
  Step 4: If any pixels remain still set at Nmax , go to Step 2.
  Step 5: The array F now holds a chamfer of the chosen subset(s).
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 17
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 0 | 255 | 255 | 255 | 255
255 | 255 | 255 | 0 | 255 | 255 | 255 | 255
255 | 255 | 255 | 0 | 255 | 255 | 255 | 255
255 | 255 | 255 | 0 | 0 | 255 | 255 | 255
255 | 255 | 255 | 0 | 0 | 0 | 0 | 255
255 | 255 | 255 | 0 | 0 | 0 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 0
0 | 0 | 0 | 1 | 1 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
  Step 2: Pass through image pixels from top to bottom and left to right.
  For a given pixel, consider neighbors above and to the left and set
  Step 3: Pass through image pixels from bottom to top and right to left.
  For a given pixel, consider neighbors bottom and to the right and set
255 | 255 | 255 | 255 | 2 | 3 | 4 | 5
255 | 255 | 255 | 0 | 255 | 255 | 255 | 255
255 | 255 | 255 | 0 | 255 | 255 | 255 | 255
255 | 255 | 255 | 0 | 255 | 255 | 255 | 255
255 | 255 | 255 | 0 | 0 | 255 | 255 | 255
255 | 255 | 255 | 0 | 0 | 0 | 0 | 255
255 | 255 | 255 | 0 | 0 | 0 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 2 | 3 | 4 | 5
255 | 255 | 255 | 0 | 1 | 2 | 3 | 4
255 | 255 | 255 | 0 | 1 | 2 | 3 | 4
255 | 255 | 255 | 0 | 1 | 2 | 2 | 3
255 | 255 | 255 | 0 | 1 | 1 | 1 | 2
255 | 255 | 255 | 0 | 0 | 0 | 0 | 1
255 | 255 | 255 | 0 | 0 | 0 | 1 | 2
4 | 3 | 2 | 1 | 1 | 1 | 2 | 3

## Slide 18: Matric and topological properties of digital images
The relationship between different distance functions and algorithm 2.1.
  Euclidean distance, city block distance, and chessboard distance
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 19: Matric and topological properties of digital images
Edge
  A local property of a pixel and its immediate neighborhood
  It is a vector given by a magnitude and direction which tell us how fast the image intensity varies in a small neighborhood of a pixel.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
https://docs.opencv.org/3.4/d0/da5/tutorial_ximgproc_prediction.html

## Slide 20: Matric and topological properties of digital images
Inner borders and outer borders of a region
  Region inner borders shown as white circles and outer borders shown as black squares (using 4-neighborhoods).
Convex region
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 21: Matric and topological properties of digital images
Convex hull
  A convex hull of a region is the smallest convex region containing the input region.
Topological (拓撲學的) properties
  Topological properties are invariant to homeomorphic (同胚 ) transforms.
  For example, rubber sheet transforms
    Imagine a small rubber balloon with an object painted on it.
    Topological properties of the object are those which are invariant to arbitrary stretching of the rubber sheet.
    Stretching does not change contiguity of the object parts and does not change the number of holes in regions.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
https://gtpreapgeometry.files.wordpress.com/2016/05/ws-topology-or-rubber-sheet-geometry.pdf

## Slide 22: Topological properties
Topology is concerned with the properties of space that are preserved under continuous deformations, such as stretching (拉伸) and bending (彎曲), but not tearing (撕開) or gluing (黏合).
Example of the topological properties: genus and connectivity (a-d) have a connectivity of 1, 1, 2, and 3 respectively(MacDonald et. al. , 1986).
https://www.researchgate.net/figure/267246393_fig10_Fig-211-Example-of-the-topological-properties-genus-and-connectivity-a-d-have-a
https://en.wikipedia.org/wiki/Topology

## Slide 23: Matric and topological properties of digital images
Topological properties
  An object with non-regular shape can be represented by a collection of its topological components.
  The set inside the convex hull which does not belong to an object is called the deficit (不足額) of convexity, including lakes and bays.
    Lakes are fully surrounded by the object.
    Bays are contiguous with the border of the convex hull of the object.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 24: Histograms
The brightness histogram of an image provides the frequency of the brightness value in the image.
Local smoothing of the histogram
  To reduce the number of local minima and maxima
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 25: Entropy
Information entropy
  The entropy can serve as an measure of ‘disorder’.
  As the level of disorder rises, entropy increases and events are less predictable.
  Assuming a discrete random variable X with possible outcomes xk, k = 1,…,n. Then the entropy defined as
  where ;
https://towardsdatascience.com/entropy-how-decision-trees-make-decisions-2946b9c18c8

## Slide 26
https://devopedia.org/images/article/168/4250.1555312917.jpg

## Slide 27: Visual perception of the image
Contrast
  Contrast is the local change in brightness and is defined as the ratio between average brightness of an object and the background.
  Conditional contrast effect
    Circles inside squares have the same brightness.
    Human perceive the brightness of the small circles as different.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 28: Visual perception of the image
Acuity (敏銳度)
  Acuity is the ability to detect details in an image.
    The human eye is less sensitive to slow and fast changes in brightness in the image plane but more sensitive to intermediate (中間的) changes.
    Acuity also decreases with increasing distance from the optical axis (光軸).
  Resolution in an image is bounded by the resolution ability of the human eye.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 29: Visual perception of the image
Some visual illusions (錯覺)
  Human perception of images is prone (易於) to many illusions.
    Object borders
      Boundaries of objects and simple patterns such as blobs or lines enable adaptation effects similar to conditional contrast.
      For example, the Ebbinghaus illusion (艾賓浩斯錯覺)
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 30: Visual perception of the image
Some visual illusions (錯覺)
  Parallel diagonal line segments which are not perceived as parallel. (left image)
  Horizontal lines are parallel, although not perceived as such. (right image)
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 31: If something is rotating – go home, you need a break!

## Slide 32: Visual illusions
https://www.chinatimes.com/realtimenews/20160704005335-262903?chdtv

## Slide 33: Visual perception of the image
Perceptual (知覺) grouping
  The human ability to group items according to various properties is illustrated in the figure.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 34: Visual perception (視覺感知) of the image
Perceptual grouping (知覺分組)
  Perceived properties (感知屬性) help people to connect elements together (in cluttered scenes) based on strongly perceived properties as parallelism, symmetry, continuity and closure (封閉性).
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 35: Image quality
Image degradation (退化;下降)
  An image might be degraded (退化) during capture, transmission, or processing.
  Measures of image quality can be used to assess the degree of degradation.
  Image degradation (影像劣化;影像衰退) model H
g(x, y): input image
f(x, y): degraded image
H: degradation process
n(x, y): noise

## Slide 36: Noise in images
Noise is one kind of image degradations.
  Noise is usually described by its probabilistic characteristics.
  White noise has a constant power spectrum.
  Gaussian noise: a special case of white noise
  where is the mean and is the standard deviation of the random variable
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
white noise:
https://zh.wikipedia.org/wiki/%E7%99%BD%E9%9B%9C%E8%A8%8A

## Slide 37: Noise in images
When an image is transmitted through some channel, noise which is usually independent of the image signal occurs.
  Additive noise model (加性雜訊模型)
  where is the noise and is the input image.
  Algorithm 2.3: Generation of additive, zero mean Gaussian noise
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 38: Algorithm 2.3: Generation of additive, zero mean Gaussian noise
Step1: Suppose an image has gray-level range .
Select ; low values generate less noise.
Step 2: For each pair of horizontally neighboring pixels , generate a pair of independent random number in the range .
Step 3: Calculate
(This is the Box-Muller transform which assumes that , are independently normally distributed with zero mean and variance )
Step 4: Set and , where is the input image.
Step 5: Set
;
Step 6: Go to Step 2 until all pixels have been scanned.

## Slide 39: Box–Muller transform
Suppose U1 and U2 are independent random variables that are uniformly distributed in the interval (0, 1). Let
and
Then Z0 and Z1 are independent random variables with a standard normal distribution.
Visualisation of the Box–Muller transform — the colored points in the unit square (u1, u2), drawn as circles, are mapped to a 2D Gaussian (z0, z1), drawn as crosses. The plots at the margins are the probability distribution functions of z0 and z1. Note that z0 and z1 are unbounded; they appear to be in [-3,3] due to the choice of the illustrated points.
https://en.wikipedia.org/wiki/Box%E2%80%93Muller_transform#cite_note-4

## Slide 40: Noise in images
Signal-to-noise ratio (SNR;信噪比)
;
  where is the noise and is the image.
  SNR represents a measure of image quality, with high values being ‘good’.
  It is often expressed in the logarithmic scale.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 41: Noise in images
Multiplicative noise model (乘性雜訊模型)
  where is the noise and is the input image.
  The noise magnitude depends in many cases on the signal magnitude itself.
  Television raster (光柵) degradation
    An example of multiplicative noise
    Degradation depends on TV lines
      In the area of a line this noise is maximal, and between two lines it is minimal.
https://taratrangmarvideoproduction.wordpress.com/2012/10/16/the-tv-lines/

## Slide 42: Noise in images
Quantization noise (量化雜訊)
  Quantization noise occurs when insufficient quantization levels are used.
  For example, 50 levels for a monochromatic (單色) image.
Impulse noise (脈衝雜訊)
  Impulse noise means that an image is corrupted with individual noisy pixels whose brightness differs significantly from that of the neighborhood.
  For example, salt-and-pepper noise (椒鹽雜訊)
    An image is corrupted with white and/or black pixels