## Slide 1: Chapter 2
The image, its representations and properties
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 2: Color images
Physics of color
  The world is colorless.
  Human color perception is carried out by the nervous system (神經系統), which interprets differently to distinct electromagnetic wavelengths (電磁波長 ).
  Electromagnetic spectrum (電磁頻譜 )
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 3: Physics of color
Visible spectral colors (可見光譜顏色 )
  Colors can be represented as combinations of the primary colors.
    Primary colors (原色): red, green and blue
    1 nm = 10-9 m
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
https://zh.wikipedia.org/wiki/%E5%8E%9F%E8%89%B2

## Slide 4: Electromagnetic spectrum

## Slide 5: Physics of color
Why do we see the world in color?
  The surface reflection (表面反射) rebounds (反彈) incoming energy from the surface, whose spectrum remains the same as that of the light source.
    It is independent of the surface (do not have a color).
  The energy diffuses (漫射) into the material and reflects randomly from the internal pigment (顏料;色素) in the matter. (body reflection)
    Observed color of objects is caused by certain wavelength absorptions (吸收) by pigment particles in dielectrics (電介質 ).
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 6: Color perceived by humans
Retina (視網膜) is composed of photoreceptors (感光器).
Two types of photoreceptors
  Rods: sensitive to intensity
  Cones: sensitive to color
  PS 視桿細胞(rod cell) v.s. 視錐細胞(cone cell)
  視桿細胞主要與暗視覺有關( 對光線的明暗變化、形態與移動特別敏感 )，分佈在視網膜周邊部。
  視錐細胞則與光視覺有關(用來辨別色彩，並適合偵測各種細節 )，分佈在視網膜中心部，中央小凹( foveola )只有視錐細胞。
  PS 眼球構造圖 https://mulicia.pixnet.net/blog/post/4213181
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 7: Color perceived by humans
Types of cones: L(red), M(green), S(blue)
  The figure shows relative sensitivity of S, M, L cones of the human eye to wavelength.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
色盲資訊 https://zh.wikipedia.org/wiki/%E8%89%B2%E7%9B%B2
http://blog.fourdesire.com/2014/12/11/wo-he-ni-you-dian-bu-yang-zhen-dui-se-mang-zhe-de-ti-tie-she-ji/
人類每隻眼球視網膜大約600萬~700萬的視錐細胞(cones)，多分布在黃斑處。大多數哺乳動物都具有能感受紅光、藍光以及綠光的三種視錐細胞。
http://cht.a-hospital.com/w/%E8%A7%86%E9%94%A5%E7%BB%86%E8%83%9E

## Slide 8: Color perceived by humans
RGB color space
  Given primary colors R, G, B, then color matching functions can be obtained by
  ;
  where may be negative.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
https://www.itp.uni-hannover.de/~zawischa/ITP/colmetr.html

## Slide 9: Color perceived by humans
CIE XYZ color space
  CIE: an organization responsible for color standard
    Commission internationale de l'éclairage (French)
    International Commission on Illumination
    國際照明委員會
  XYZ
    Y: brightness (luminance)
    The actual color is a mixture of
  where are weights in the mixture
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
CIE XYZ color space
https://zh.wikipedia.org/wiki/CIE1931%E8%89%B2%E5%BD%A9%E7%A9%BA%E9%97%B4

## Slide 10: Color perceived by humans
Color gamut (色域)
  The subspace of colors perceivable by humans is called the color gamut.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
https://personalaudio.hk/2017/08/04/colors/

## Slide 11: Color perceived by humans
The CIE 1931 color space chromaticity diagram (色度圖)
  CIE chromaticity diagram is a projection of XYZ color space into a plane.
  The triangle depicts a subset of colors spanned by red, green, and blue. These are TV colors, i.e., all possible colors, which can be seen on a CRT display.
  Given X, Y, Z, then x, y, z can be obtained by
  ;
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 12: Color perceived by humans
Display and printing devices use three selected real primary colors (原色;基色).
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 13: Color spaces
RGB color space
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 14
RGB color spaces

## Slide 15: Color spaces
One of the transformations between RGB and XYZ color space
An XYZ to RGB conversion
An RGB to XYZ conversion
https://www.w3schools.com/colors/colors_converter.asp
https://www.rapidtables.com/convert/color/index.html

## Slide 16: Color spaces
  CMY color model uses subtractive color mixing which is used in printing processes.
  Cyan (青綠色), magenta (洋紅色), and yellow (黃色) are the secondary colors (二次色) of light of the primary colors (原色) of pigments (顏料).
  An RGB to CMY conversion

## Slide 17: Color spaces
  CMYK (K: black) stores ink values for black in addition.
減色法https://zh.wikipedia.org/wiki/%E6%B8%9B%E8%89%B2%E6%B3%95

## Slide 18
Additive color (加色法)
https://zh.wikipedia.org/wiki/%E5%8A%A0%E8%89%B2%E6%B3%95
https://zh.wikipedia.org/wiki/%E6%B8%9B%E8%89%B2%E6%B3%95
Subtractive color(減色法)
減色法模型解釋了塗料，染料，墨水和天然色素的混合物產生的顏色，每個顏色會減去（即吸收）某些波長的光並向其他反射。表面所顯示的顏色取決於它反映在電磁波譜的顏色。
加色法是描述那些由不同顏色的光混合形成新顏色的情形。
Color Fundamentals
https://en.wikipedia.org/wiki/Additive_color

## Slide 19: Color spaces
HSV color model (Hue, Saturation, and Value)
  HSV color model is illustrated as a cylinder.
  HSV v.s. HSL: https://en.wikipedia.org/wiki/HSL_and_HSV
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 20
Color Models -- HSI Model
H: Hue
S: Saturation
I: Intensity

## Slide 21
https://nerd.nu/forums/topic/2632-forum-game-google-image-war/?page=7
Color Models -- HSI Model

## Slide 22
Figure 6.15 shows the hue, saturation, and intensity images for the RGB values shown in Figure 6.8.
H
S
I
Color Models -- HSI Model

## Slide 23
Color Models -- HSI Model
H
S
I

## Slide 24
Color Models -- HSI Model
H
S
I

## Slide 25
Color Transformations
RGB<->HSI<->CMYK

## Slide 26
Color Complement Transformations

## Slide 27: Palette images
Palette images (indexed images;調色板) provide a simple way to reduce the amount of data needed to represent an image.
  The pixel values constitute a link to a lookup table (palette; 調色板).
  The table contains as many entries as the range of possible values in the pixels which is typically 8 bits (256 values).
  For example, (8-bit color, with three bits of red, three bits of green, and two bits of blue)

## Slide 28: Palette images
http://www.technologyuk.net/computing/computer-systems/display-adapter.shtml

## Slide 29: Color constancy
Color constancy (顏色恆定)
  Surfaces have different colors and brightness when viewed under different lights.
  The human vision system is able to abstract to a certain degree from the illumination changes and perceive several instances of a particular color as the same.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 30: Visual illusions VS Color constancy
https://www.youtube.com/watch?v=-sAoJgJUA8Y
https://www.youtube.com/watch?v=z9Sen1HTu5o